## Slide 1: DATA COMMUNICATION NETWORKS

## Slide 2: A Communications Model
Source
  generates data to be transmitted
Transmitter
  Converts data into transmittable signals
Transmission System
  Carries data
Receiver
  Converts received signal into data
Destination
  Takes incoming data

## Slide 3: Communications Tasks
Transmission system utilization | Addressing
Interfacing | Routing
Signal generation | Recovery
Synchronization | Message formatting
Exchange management | Security
Error detection and correction | Network management
Flow control | 

## Slide 4: Simplified Communications Model - Diagram

## Slide 5: Simplified Data Communications Model

## Slide 6: Basic Concepts

## Slide 7: TRANSMISSION MODES
Simplex
Half Duplex
Full Duplex

## Slide 8: Networks: key issues
Network criteria
  Performance
    Throughput
    Delay
  Reliability
    Data transmitted are identical to data received.
    Measured by the frequency of failure
    The time it takes a link to recover from a failure
  Security
    Protecting data from unauthorized access

## Slide 9: Categories of Topology

## Slide 10: Mostly used network topologies
mesh
star
bus
ring

## Slide 11: A hybrid topology: a star backbone with three bus networks

## Slide 12: Networking
Point to point communication not usually practical
  Devices are too far apart
  Large set of devices would need impractical number of connections
Solution is a communications network
  Wide Area Network (WAN)
  Local Area Network (LAN)

## Slide 13: Network Types (based on Scale)
Local Area Networks (LANs) - room, building
  a group of PCs that share a circuit.
Backbone Networks - less than few kms
  a high speed backbone linking the LANs at various locations.
Metropolitan Area Networks (MAN) - (< few 10 kms)
  connects LANs and BNs at different locations
  leased lines or other services used to transmit data.
Wide Area Networks (WANs) - (> few 10 kms)
  Same as MAN except wider scale

## Slide 14: OSI
Open Systems Interconnection
Developed by the International Organization for Standardization (ISO)
Seven layers
A theoretical system delivered too late!
TCP/IP is the de facto standard

## Slide 15: The OSI Environment

## Slide 16
TCP/IP and the OSI Model

## Slide 17: OSI v TCP/IP

## Slide 18: IEEE 802 Focus
OSI Reference
  Data Link layer
  Physical layer
Areas
  Network cards and cables
  Network electronic/optical/ wireless communication standard as they apply to the lower two layers mentioned above
  WAN connectivity

## Slide 19: IEEE 802 Committees And Responsibilities
802.1
  Internetworking
802.2
  Logical Link Control (LLC)
802.3
  CSMA/CD
802.4
  Token Bus LAN

## Slide 20: IEEE 802 Committees and Responsibilities (Cont.)
802.5
  Token Ring LAN
802.6
  Metropolitan Area Network
802.7
  Broadband Technical Advisory Group
802.8
  Fiber-Optic Technical Advisory Group

## Slide 21: IEEE 802 (Cont.)
802.9
  Integrated Voice/Data Networks
802.10
  Network Security
802.11
  Wireless Networks
802.12
  Demand Priority Access LANs
  Ex: 100BaseVG-AnyLAN

## Slide 22: INTERNETWORKING PROTOCOL
It is unreliable and connectionless datagram protocol.
The IP provides no error checking or tracking.
IP transports data in Packets called datagrams , each of which transported separately.
Datagrams can travel along different routes and can arrive out of sequence or be duplicated.
IP does not keep track of the routes and has no facility for reordering datagrams once they arrive at their destination.

## Slide 23
IP Datagram

## Slide 24: Different types of address
Three different levels of addresses are used in an internet using TCP/IP protocols:
  Physical Address
  Logical Address
  Port Address

## Slide 25: Physical Address
It is also known as link address.
It is defined by its LAN or WAN.
It is lowest level address.
It can be either
  Unicast ( One single recipient)
  Multicast (a group of a recipients)
  Broadcast ( To be received by all systems in the network.)
Some networks supports all three addresses.

## Slide 26: Addressing

## Slide 27: Logical Address
The logical addresses are designed for internetwork communication.
It is currently 32-bit address that can uniquely define a host connected to the internet.
It can be either unicast, broadcast or multicast.

## Slide 28: Port Address
IP address and physical address are necessary for source to destination host transmission.
The aim of internet communication is a process communicating with the another process.
For example,
  Computer A can communicate with C by TELNET
  Computer A communicate with B by FTP.
For these process occur simultaneously, each process should be labeled. They are labeled by an address called port address.

## Slide 29: Addressing

## Slide 30: Class ranges if Internet Addresses

## Slide 31
Given the network address 132.21.0.0, find the
class, the block, and the range of the addresses
The 1st byte is between 128 and 191.
Hence, Class B
The block has a netid of 132.21.
The addresses range from
132.21.0.0 to 132.21.255.255.

## Slide 32: IPv6
IPv6 (Internet Protocol version 6) is a set of specifications from the Internet Engineering Task Force (IETF) that's essentially an upgrade of IP version 4 (IPv4).
32 bits to 128 bits.
2^128 = 340,282,366,920,938,463,463,374,607,431,768,211,456
And a new type of address called an "anycast address" is defined,
used to send a packet to any one of a group of nodes.
Authentication and Privacy Capabilities Extensions to support authentication, data integrity, and (optional) data confidentiality are specified for IPv6.

## Slide 33: IPv6 Address Scheme :
An IP packet contains several types of information, as
illustrated.